## Slide 1
A GPU-Based Fast SPH Solver for Granular Material and Fluid Simulation
Huzaifa Unjhawala, Nevindu Batagoda, Luning Bakke, Lijing Yang, Radu Serban and Dan Negrut
unjhawala@wisc.edu
University of Wisconsin-Madison
Chrono::FSI – SPH-Based Multiphysics
Acknowledgements: This work was carried out in part with support from US Army project US ARO W911NF1910431 and National Science Foundation projects CISE1835674, and OAC2209791.
Smoothed Particle Hydrodynamics (SPH) discretizes the mass balance and momentum conservation equations
SPH approximates a function based on a spatial average of adjacent sampling points – Proximity Search
Fluid-Structure interaction enabled through Boundary Condition Enforcing (BCE) markers.
Solver can be used for 2 kinds of physics
Fluid – Navier Stokes
Granular Material – Using rheology presented in [1]
[1] Dunatunga, S and Kamrin, K. "Continuum modelling and simulation of granular flows through their many phases." Journal of Fluid Mechanics 779 (2015): 483-513.
[2] Hu, Wei, Pei Li, Arno Rogg, Alexander Schepelmann, Colin Creager, Samuel Chandler, Ken Kamrin, and Dan Negrut. "Using physics-based simulation towards eliminating empiricism in extraterrestrial terramechanics applications." arXiv preprint arXiv:2405.11001 (2024).
[3] Hu, Wei, Milad Rakhsha, Lijing Yang, Ken Kamrin, and Dan Negrut. “Modeling Granular Material Dynamics and Its Two-Way Coupling with Moving Solid Bodies Using a Continuum Representation and the SPH Method.” Computer Methods in Applied Mechanics and Engineering 385 (2021): 114022. https://doi.org/10.1016/j.cma.2021.114022.
The Math – Granular Material Edition
Cauchy Stress
Jaumann derivative
Material Constants
Rotation Rate
Plastic Strain Rate
Elastic Strain Rate
Drucker-Prager Friction Coefficient
Plastic Regime
Elastic Regime
[1]
Both Granular and Fluid Simulations are well validated
Granular Scaling Laws satisfied in simulator [2]
Viper drawbar pull tests match experimental data
Against empirical results with simple tests[3]
Sphere drop
Cone penetration matches experimental data in [4]
Poiseuille Flow
We optimized the proximity search and made the code 2x faster!
2x Faster, Same Accuracy
2x Faster, Same Accuracy
You can “see” the SPH Terrain with Chrono::Sensor too!
Piston based Wave Maker
Old Code
New Code
RASSOR on SPH-based Terrain
MGRU Rover Slip-Slope Test
Old Code
New Code
Old Code
New Code
Flexible Plate against a Dam Break
Old Code
New Code
These are images captured using the Chrono camera sensor.
User can control exposure, aperture, type of lens, lens flare, lens vignetting, capture motion blur, account for light transport on the moon, inject sensor noise, etc.