## Slide 1
FNODE: Flow-Matching for data-driven simulation of constrained multibody systems
Hongyu Wang¹, Jingquan Wang¹, Dan Negrut¹
¹University of Wisconsin-Madison
Introduction
• Multibody dynamics is vital in engineering and science.
• Used in robotics, vehicle dynamics, and biomechanics.
• Traditional methods face challenges with complex dynamics.
• Machine learning offers data-driven simulation.
• LSTM and FCNNs struggle with long-term predictions.
• Neural ODEs face computational bottlenecks.
• Flow-matching algorithms improve learning vector fields.
• FNODE enhances efficiency and accuracy.
Methodology
• FNODE uses multibody dynamics with Lagrange multipliers for constraints.
• Operates on an augmented state space to model acceleration directly.
• Eliminates the need for ODE solvers in backpropagation.
• Improves computational efficiency while maintaining accuracy.
• Uses FFT-based spectral differentiation for periodic systems.
• Finite difference methods are applied for non-periodic datasets.
• Trained with Adam optimizer for stable convergence.
Numerical Experiments
• FNODE evaluated on multiple benchmarks: single and triple mass-spring-damper systems, double pendulum, slider-crank, and cartpole.
• Outperformed MBD-NODE, LSTM, and FCNN in accuracy, generalization, and computational efficiency.
• In single-mass-spring-damper system, FNODE maintained close agreement with ground truth.
• FNODE achieved best accuracy in chaotic double pendulum benchmark despite error accumulation.
• Demonstrated ability to maintain accurate long-term predictions in slider-crank mechanism.
• FNODE's performance highlights its robustness across various dynamic systems.
Discussion
• FNODE trains faster than MBD-NODE by avoiding adjoint sensitivity.
• Achieves lower prediction error compared to black-box baselines.
• Scalable for data-driven simulation of constrained multibody systems.
• Bypasses embedding an ODE solver in backpropagation.
• Competitive with MBD-NODE in terms of accuracy.
• Potential for higher-dimensional and contact-rich systems.
Conclusions
• FNODE models multibody dynamics with data-driven methods.
• Learns accelerations, removing the adjoint bottleneck.
• Trains faster, outperforming LSTM and FCNN baselines.
• Offers high accuracy and multiscale robustness.
• Future work: noise-resilient acceleration estimation.
• Applications in PDE systems and closed-loop control.